## Slide 1
What Every Computational Physicist Should Know About Computer Architecture*
Ian A. Cosden, Ph.D.
icosden@princeton.edu Manager, HPC Software Engineering and Performance Tuning
Research Computing, Princeton University
CoDaS-HEP Summer School
July 22, 2019
a[i]
b[i]
a[i]+b[i]
a[i+1]
b[i+1]
a[i+1]+b[i+1]
a[i+2]
b[i+2]
a[i+2]+b[i+2]
a[i+3]
b[i+3]
a[i+3]+b[i+3]
+
=
*Plus some other useful technology

## Slide 2: Outline
Motivation
HPC Cluster
Compute
Memory
Disk
Emerging Architectures

## Slide 3: Why Care About the Hardware?
Get the most out of this week
Be able to ask better questions and understand the answers
Architecture changes can force new design and implementation strategies
  Prevent programming mistakes
  Make educated decisions
Exploit the hardware to your advantage (performance)

## Slide 4: Hardware is the Foundation
User
Program
System
Hardware
Application
Programming Language
Programming Models
Compiler
Runtime Libraries
OS support for resource management (threading, memory, scheduling)
Shared Memory
CPU
CPU
Disk
Accelerators
Network

## Slide 5: Why Care About HPC Hardware?
High-Performance Computing (HPC)
  Aggregate computing power in order to deliver far more capacity than a single computer
  Supercomputers
Some problems demand it from the onset
Many problems evolve to need it
  When you outgrow your laptop, desktop, departmental server
  Need to know capabilities and limitations
  Lots of High-Throughput Computing (HTC) jobs run on HPC clusters
HPC
HTC

## Slide 6: Moore’s Law
Number of transistors doubles ever 18-24 months
More transistors = better, right?

## Slide 7: The Free Lunch is Over
https://www.karlrupp.net/2015/06/40-years-of-microprocessor-trend-data/
The Free Lunch
Vectorization
Parallelization

## Slide 8: Top 500 Supercomputers
https://www.nextplatform.com/2016/06/20/china-topples-united-states-top-supercomputer-user/
https://www.top500.org

## Slide 9: Why Talk About Intel Architecture?
https://www.revolvy.com/page/TOP500

## Slide 10: Outline
Motivation
HPC Cluster
Compute
Memory
Disk
Emerging Architectures

## Slide 11: Zoom In On A Cluster
A cluster is just connected collection of computers called nodes
A single-unconnected node is usually called a server
Entire clusters and stand-alone servers are sometimes referred to as machines

## Slide 12: Parallel Computers
HPC Cluster
  A collection of servers connected to form a single entity
      Each is essentially a self-contained computer
      OS with CPU, RAM, hard drive, etc.
  Stored in racks in dedicated machine rooms
  Connected together via (low latency) interconnects
    Ethernet < Infiniband, OPA (Intel’s Omi-Path Architecture)
  Connected to storage
  Vast majority of HPC systems
SMP System
  Symmetric Multi-Processing
  CPUs all share memory – essentially one computer
  Expensive and serve unique purpose
    Huge memory and huge OpenMP jobs
Princeton’s Della Cluster

## Slide 13: Basic Cluster Layout
Compute Nodes
Login Node(s)
Shared Storage
Scheduler
Your Laptop
ssh

## Slide 14: Nodes Are Discrete Systems
Memory address space
  Range of unique addresses
Separate for each node
Can’t just access all memory in cluster
Each node has a separate address space
Network
Memory
Core
Core
Core
Core
Memory
Core
Core
Core
Core
Memory
Core
Core
Core
Core
Memory
Core
Core
Core
Core

## Slide 15: Clusters With Accelerators
GPU / KNL
GPU / KNL
GPU / KNL
GPU / KNL
Accelerators: GPUs or Xeon Phi (KNC, KNL)
Programmable with MPI + x
    Where x = OpenMP, OpenACC, CUDA, …
    Or x = OpenMP + CUDA, …
    Increase computational power
      Increase FLOPS / Watt
    Top500.org
      Shift toward systems with accelerators a few years ago

## Slide 16: Outline
Motivation
HPC Cluster
Compute
Memory
Disk
Emerging Architectures

## Slide 17: Multicore Processors
(Most) modern processors are multicores
  Intel Xeon
  IBM Power
  AMD Opteron
  ARM processors
  Mobile processors
Most have vector units
Most have multiple cache levels
Require special care to program (multi-threading, vectorization, …)
  Free lunch is over!
Instruction set
  x86_64 – Intel and AMD
  Power, ARM, NVIDIA, etc have different instruction sets
Intel Skylake Architecture

## Slide 18: Motherboard Layout
Typical nodes have 1, 2, or 4 Processors (CPUs)
  1: laptop/desktops/servers
  2: servers/clusters
  4: high end special use
Each processor is attached to a socket
Each processor has multiple cores
Processors connected via interconnect
Memory associated with processor
  Programmer sees single node memory address space
Processor
Core
Core
Core
Core
Interconnect
Intel: QPI/UPI
AMD: HT

## Slide 19: Motherboard Layouts
Symmetric MultiProcessing (SMP)
front side bus (FSB) bottlenecks in SMP systems, device-to-memory bandwidth via north bridge, north bridge to RAM bandwidth limitations.
Non-Uniform Memory Access (NUMA)
physical memory partitioned per CPU, fast interconnect to link CPUs to each other and to I/O.
Remove bottleneck but memory is no longer uniform – 30-50% overhead to accessing remote memory, up to 50x in obscure multi-hop systems.
Elmer / Tuura /
Lefebvre
Intel QPI/UPI,
AMD HT

## Slide 20: Example: Intel Skylake CPU
Core
Core
Core
Core
Core
Core
Core
Core
Core
Memory
Controller
DDR
UPI, PCIe, DMI
Core Definition (Jarp):
“A complete ensemble of execution logic, and cache storage as well as register files plus instruction counter (IC) for executing a software process or thread.”
Memory Controller
UPI – Intel UltraPath Interconnect
PCIe – Peripheral Component Interconnect Express
DMI – Direct Media Interface
DDR – Double Data Rate
Lefebvre

## Slide 21: Skylake Core Microarchitecture
Key Components:
Control logic
Register file
Functional Units
          ALU (arithmetic and logic unit)
          FPU (floating point unit)
          Data Transfer
            Load / Store
Too much!

## Slide 22: Vectorization Terminology
SIMD: Single Instruction Multiple Data
New generations of CPUs have new capabilities
  Each core has VPUs and vector registers
  Machine (assembly) commands that take advantage of new hardware
    Called “instruction set”
E.g. Streaming SIMD Extensions (SSE) & AVX: Advanced Vector Extension (AVX)
a[i]
b[i]
+
a[i]+b[i]
=
a[i]
b[i]
a[i]+b[i]
a[i+1]
b[i+1]
a[i+1]+b[i+1]
a[i+2]
b[i+2]
a[i+2]+b[i+2]
a[i+3]
b[i+3]
a[i+3]+b[i+3]
+
=
Vector (SIMD)
One operation
One result
One operation
Multiple results
Scalar (SISD)
for (int i=0; i<N; i++) {
c[i]=a[i]+b[i]; }
At inner-most loop level

## Slide 23: HPC Performance Metrics
FLOP = Floating-point Operation
FLOPs = Floating-point Operations
FLOPS = Floating-point Operations Per Second
  Often FLOP/sec to avoid ambiguity
FLOPS/$
FLOPS/Watt
Bandwidth: GB/s
Calculation for single processor
  Usually Double Precision (64-bit)
  FLOPS = (Clock Speed) *(Cores)*(FLOPs/cycle)
N.B. - not to be confused with a Hollywood flop!
Notes: 1999 Film
Lost ~100 million

## Slide 24: Intel Xeon (Server) Architecture Codenames
Number of FLOP/s depends on the chip architecture
Double Precision (64 bit double)
  Nehalem/Westmere (SSE):
    4 DP FLOPs/cycle: 128-bit addition + 128-bit multiplication
  Ivybridge/Sandybridge (AVX)
    8 DP FLOPs/cycle: 256-bit addition + 256-bit multiplication
  Haswell/Broadwell (AVX2)
    16 DP FLOPs/cycle: two, 256-bit FMA (fused multiply-add)
  KNL/Skylake (AVX-512)
    32 DP FLOPs/cycle: two*, 512-bit FMA
  Cascade Lake (AVX-512 VNNI with INT8)
    32 DP FLOPs/cycle: two, 512-bit FMA
FMA = (a × b + c)
Twice as many if single precision (32-bit float)
*Some Skylake-SP have only one
Notes: Intel Deep Learning Boost (VNNI) provides significant, more efficient deep learning inference acceleration
Combines three AVX-512 instructions (VPMADDUBSW, VPMADDWD, VPADDD) into a single VPDPBUSD operation

## Slide 25: Outline
Motivation
HPC Cluster
Compute
Memory
  Layout
  Cache
  Performance
Disk
Emerging Architectures

## Slide 26: Memory Hierarchy
Main Memory (DRAM)
Core
1
L1
L3
L2
Core
2
L1
L2
Core
n
L1
L2
…
UPI
Main Memory (DRAM)
L3
L2
L2
L2
L1
L1
L1
Core
1
Core
2
Core
n
…
Dual Socket Intel Xeon CPU
 | Registers | L1 Cache | L2 Cache | L3 Cache | DRAM | Disk
Speed | 1 cycle | ~4 cycles | ~10 cycles | ~30 cycles | ~200 cycles | 10ms
Size | < KB per core | ~32 KB per core | ~256 KB per core | ~35 MB per socket | ~100 GB per socket | TB
CPU 1
CPU 2
Notes: DDR4 – Double data rate 4th generation (Synchronous dynamic RAM)
UPI – UltraPath Interconnect (Intel) Skylake shifted more L2 cache from shared L3 cache (L2 ~1MB)

## Slide 27: Does It Matter?
http://web.sfc.keio.ac.jp/~rdv/keio/sfc/teaching/architecture/architecture-2008/hennessy-patterson/Ch5-fig02.jpg
Gap grows at 50% per year!
If your data is served by RAM and not caches it doesn’t matter if you have vectorization.
To increase performance, try to minimize memory footprint.
Notes: Memory gap increases…
What do you think should require more attention?

## Slide 28: Outline
Motivation
HPC Cluster
Compute
Memory
Disk
  Types
  Filesystems
Emerging Architectures

## Slide 29: File I/O
“A supercomputer is a device for turning compute-bound problems into I/O-bound problems.”
-- Ken Batcher, Emeritus Professor of Computer Science at Kent State University

## Slide 30: Types of Disk
Hard Disk Drive (HDD)
  Traditional Spinning Disk
Solid State Drives (SSD)
  ~5x faster than HDD
Non-Volatile Memory Express (NVMe)
  ~5x faster than SSD
Photo Credit: Maximum PC

## Slide 31: Types of Filesystems - NFS
NFS – Network File System
  Simple, cheap, and common
  Single filesystem across network
  Not well suited for large throughput
Storage
Storage
Storage
NFS Server
Head node
Comp node 001
Comp node 002
Comp node N
...
...
≤ 8 storage devices

## Slide 32: Parallel Filesystems
GPFS (General Parallel Filesystem – IBM)
  Designed for parallel read/writes
  Large files spread over multiple storage devices
  Allows concurrent access
  Significantly increase throughput
Lustre
  Similar idea
  Different implementation
Parallel I/O library in software
  Necessary for performance realization
Storage
Storage
Storage
Object Storage
Head node
Comp node 001
Comp node 002
Comp node N
...
...
File A 1/3
File A 2/3
File A 3/3
GPFS Servers
File A
1,000s of storage devices

## Slide 33: Outline
Motivation
HPC Cluster
Compute
Memory
Disk
Emerging Architectures
  Xeon Phi
  GPU
  Cloud

## Slide 34: Emerging Architectures
The computing landscape changes rapidly
110 TOP500 systems have accelerators (June 2018)
https://www.top500.org/statistics
Notes: NVIDIA P100, Intel Xeon Phi

## Slide 35: Intel Xeon Phi a.k.a. Intel MIC
MIC: Many Integrated Cores
x86-compatible multiprocessor architecture
Programmable using
  C, C++, Fortran
  MPI, OpenMP, OpenCL, …
Started as co-processor
  Data travels over PCIe
Became a main processor in 2nd generation
Merged into Xeon line ~1 year ago
  Intel announced end of Xeon Phi product line

## Slide 36: GPUs
Graphic Processing Unit (GPU)
  General Purpose GPU (GPGPU)
Exclusively a co-processor
  Data travels over PCIe
  NVLink is NVIDIAs new high-speed interconnect
Not compatible with x86 library
Programmable using:
  CUDA, OpenCL
  OpenACC, OpenMP
NVIDIA GPUs
  Fermi/Kepler/Maxwell/Pascal/Volta
NVIDIA Volta V100

## Slide 37: NVIDIA Volta (V100) GPU
Scalar Processors execute parallel thread instructions
Streaming Multiprocessors (SMs) each contain:
  64 SP units (“CUDA cores”)
  32 DP unit
32 GB device memory
Execution Model:
Notes: LD/ST units
FP16 @ 2x SP rate
cc7.0:
TensorCore
4 warp schedulers
Each warp scheduler is dual issue capable
P100: 50 SM’s, 16GB
V100: 80 SM’s, 16/32GB

## Slide 38: Accelerator Comparison
Lefebvre
 | Xeon Gold 5122 | Xeon Platinum 8280M | Xeon Phi 7290F | NVIDIA V100
Cores | 4 | 28 | 72 | 84 SMs
Logical Cores | 8 | 56 | 288 | 5120 cores
Clock rate | 3.6 – 3.7 GHz | 2.5 – 3.8 GHz | 1.5-1.7 GHz | 1530 MHz
Theoretical GFLOPS (double) | 460.8 | 2240 | 3456 | 7450
SIMD width | 512 bit | 512 bit | 512 bit | Warp of 32 threads
Memory | -- | -- | 16 GB MCDRAM 384 GB DDR4 | 32 GB
Memory B/W | 127.8 GB/s | 127.8 GB/s | 400+ GB/s (MCDRAM) 115.2 GB/s | 900 GB/s
Approx. Unit Price | $1,200 | $12,000 | $3,400 | $9,000
Notes: https://www.v-t.co.jp/product/wp-content/uploads/sites/2/2017/09/Skylake-SP_Feature_092017.pdf
Choice of xeon is arbitrary (actually depends on the data I could find)

## Slide 39: Demystifying the Cloud
“Regular” computers, just somewhere else
Provide users with remote virtual machines or containers
Can be used for anything:
  Mobile-services, Hosting websites, Business Application, …
  Data Analysis, High Performance Computing
Providers
  Major players: Amazon, Google, Microsoft, HP, IBM, Salesforce.com, …
  Lots of others
M. Lefebvre

## Slide 40: Cloud Computing
Advantages:
  Potentially lower cost:
    Pay as you go
  Potentially lower cost:
    Save on sysadmins and infrastructure
  Potentially lower cost:
    Economy of scale: providers
  Scaling up or down as needed
    Can be used to run overflow from a regular data center
  Access to a wide range of hardware
Additional challenges
  Data movement
    Expensive and time consuming
  Security, privacy, …
M. Lefebvre
Notes: Notice the “potentially”s

## Slide 41: What We Didn’t Talk About
Microarchitecture details (ALU, FPU, pipelining…)
Memory bandwidth
Cache lines and cache coherence
IBM (Power) or AMD
FPGAs

## Slide 42: Resources & References
Very nice glossary: https://cvw.cac.cornell.edu/main/glossary
J. Hennessy, D. Patterson, Computer Architecture: A Quantitative Approach, 6th edition (2017), ISBN 978-0128119051
U. Drepper, What Every Programmer Should Know About Memory, http://people.redhat.com/drepper/cpumemory.pdf
NVIDIA Volta Architecture Whitepaper https://images.nvidia.com/content/volta-architecture/pdf/volta-architecture-whitepaper.pdf
Notes: Bit.ly/2019-comp-arch