## Slide 1: What Every Computational Physicist Should Know About Computer Architecture*
Ian Cosden, Princeton University
Steve Lantz, Cornell University
CoDaS-HEP Summer School, August 1, 2022
a[i]
b[i]
a[i]+b[i]
a[i+1]
b[i+1]
a[i+1]+b[i+1]
a[i+2]
b[i+2]
a[i+2]+b[i+2]
a[i+3]
b[i+3]
a[i+3]+b[i+3]
+
=
*Plus some other useful technology

## Slide 2: Outline
Motivation
HPC Cluster
Compute
Memory
Disk
Other Architectures

## Slide 3: Why Care About the Hardware?
Get the most out of this week
Be able to ask better questions and understand the answers
Architecture changes can force new design and implementation strategies
  Prevent programming mistakes
  Make educated decisions
Exploit the hardware to your advantage (performance)

## Slide 4: Hardware is the Foundation
User
Program
System
Hardware
Application
Programming Language
Programming Models
Compiler
Runtime Libraries
OS support for resource management (threading, memory, scheduling)
Shared Memory
CPU
CPU
Disk
Accelerators
Network

## Slide 5: Why Care About HPC Hardware?
High-Performance Computing (HPC)
  Aggregate computing power in order to deliver far more capacity than a single computer
  Supercomputers
Some problems demand it from the onset; many problems evolve to need it
  When you outgrow your laptop, desktop, departmental server
  Ask: do you need greater capability, or just capacity?
  Either way, HPC clusters run lots of High-Throughput Computing (HTC) jobs
HPC
HTC

## Slide 6: Moore’s Law
Number of transistors doubles ever 18-24 months
More transistors = better, right?
6

## Slide 7: The Free Lunch is Over
https://www.karlrupp.net/2015/06/40-years-of-microprocessor-trend-data/
The Free Lunch
Vectorization
Parallelization

## Slide 8: Top 500 Supercomputers
https://www.nextplatform.com/2016/06/20/china-topples-united-states-top-supercomputer-user/
https://www.top500.org

## Slide 9: Why Talk About Intel Architecture?
https://en.wikipedia.org/wiki/TOP500

## Slide 10: Outline
Motivation
HPC Cluster
Compute
Memory
Disk
Other Architectures

## Slide 11: Zoom In On A Cluster
A cluster is just connected collection of computers called nodes
The high-speed network that connects the cluster is called the interconnect
A single, unconnected node is usually just called a server
Entire clusters, as well as stand-alone servers, are sometimes referred to as machines

## Slide 12: Parallel Computers
HPC Cluster: the vast majority of HPC systems
  A collection of servers connected to form a single entity
      Each is essentially a self-contained computer
      OS with CPU, RAM, hard drive, etc.
  Stored in racks in a dedicated machine room
  Networked together a via low-latency interconnect
    Ethernet < InfiniBand, Omni-Path (Intel)
  Interconnect extends to shared storage
SMP System: Symmetric Multi-Processing
  CPUs all share memory – essentially one computer
  Expensive, likely needed for a unique purpose
    Huge memory, huge OpenMP jobs
Princeton’s Della Cluster

## Slide 13: Basic Cluster Layout
Compute Nodes
Login Node(s)
Shared Storage
Scheduler
Your Laptop
ssh
SWITCHES

## Slide 14: Nodes Are Discrete Systems
Memory address space
  Range of unique addresses
Separate for each node
Can’t just access all memory in cluster
Each node has a separate address space
Network
Memory
Core
Core
Core
Core
Memory
Core
Core
Core
Core
Memory
Core
Core
Core
Core
Memory
Core
Core
Core
Core

## Slide 15: Clusters With Accelerators
“Heterogeneous” system architecture
Accelerators: GPUs, typically
  Or FPGAs, etc.
  Node can have multiple accelerators
Programmable with MPI + x
  Where x = OpenMP, OpenACC, CUDA, …
Increases computational power
  Increases FLOPS / Watt
Trending in Top500.org
  Strong shift toward systems with accelerators started ~10 years ago
GPUs
GPUs
GPUs
GPUs

## Slide 16: Outline
Motivation
HPC Cluster
Compute
Memory
Disk
Other Architectures

## Slide 17: Multicore Processors
Nearly all modern processors are multicores
  In servers: Intel Xeon, AMD EPYC, IBM Power
  In laptops: Intel, AMD, ARM
  In GPUs, phones, and mobile devices as well
Most have vector units, multiple cache levels
Require special care to program
  Multi-threading, vectorization, …
  The free lunch is over!
Instruction sets can vary
  Intel and AMD: x86_64 base, not identical
  IBM Power, ARM, NVIDIA, etc. all differ
Intel Skylake Architecture

## Slide 18: Motherboard Layout
Typical nodes have 1, 2, or 4 processors
  1: laptop/desktops/servers
  2: servers/clusters
  4 (or more): high end special use
Each processor is attached to a socket
Each processor has multiple cores
CPU can refer to a core... or a processor
Processors connected via interconnect
Memory attached to processor/socket
  Programmer sees single node memory address space
Processor
Core
Core
Core
Core
Interconnect
Intel: QPI/UPI
AMD: HT

## Slide 19: Motherboard Layouts, Past and Present
Symmetric MultiProcessing (SMP) –
Memory access is uniform, as all traffic goes via north bridge, but is bottlenecked by front side bus (FSB) and north-bridge-to-RAM bandwidth limitations. Current motherboards have no north bridge; the south bridge is now referred to as the I/O hub or just the chipset.
Non-Uniform Memory Access (NUMA) –
Physical memory is partitioned per CPU, with a fast interconnect to link CPUs to each other and to I/O.
This removes bottlenecks but memory is no longer uniform – there may be 30-50% extra latency to access remote memory, more in multi-hop systems.
Intel QPI/UPI,
AMD HT

## Slide 20: Example: Intel Skylake Scalable Processor
“System on a Chip” (SoC)
Core: “A complete ensemble of execution logic, and cache storage as well as register files plus instruction counter (IC) for executing a software process or thread.” (Jarp)
UPI – Intel Ultra Path Interconnect
PCIe – Peripheral Component Interconnect Express
DDR – Double Data Rate
DDR
North Cap: UPI, PCIe,…
Memory
Controller
Core
Core
Core
Core
Core
Core
Core
Core
Core
https://en.wikichip.org/wiki/intel/microarchitectures/skylake_(server)#High_Core_Count_.28HCC.29

## Slide 21: Skylake Core Microarchitecture
Key Components:
Control logic
Register file
Functional Units
          ALU (arithmetic and logic unit)
          FPU (floating point unit)
          Data Transfer
            Load / Store
Too much!

## Slide 22: Vectorization Terminology
New generations of CPUs add capabilities and instructions
  Each core can have one or more vector processing units (VPUs) and vector registers
  Machine (assembly) commands are often added to take advantage of new hardware
Vector instructions are also called SIMD = Single Instruction Multiple Data
  x86_64 has Streaming SIMD Extensions (SSE), Advanced Vector Extensions (AVX)
a[i]
b[i]
+
a[i]+b[i]
=
a[i]
b[i]
a[i]+b[i]
a[i+1]
b[i+1]
a[i+1]+b[i+1]
a[i+2]
b[i+2]
a[i+2]+b[i+2]
a[i+3]
b[i+3]
a[i+3]+b[i+3]
+
=
Vector (SIMD)
One operation
One result
One operation
Multiple results
Scalar (SISD)
for (int i=0; i<N; i++) {
c[i]=a[i]+b[i]; }
At inner-most loop level

## Slide 23: HPC Performance Metrics
FLOP = Floating-point Operation
  FLOPs = Floating-point Operations
  FLOPS = Floating-point Operations Per Second
  Often write FLOP/s or FLOP/sec to avoid ambiguity
Calculation for single processor
  Typically Double Precision (64-bit)
  FLOPS = (Clock Speed)*(Cores)*(FLOPs/cycle)
FLOPS/$, FLOPS/Watt are useful metrics too
Bandwidth metrics (“giga” usually means 109)
  GB/s = gigabytes/sec
  Gb/s = gigabits/sec
N.B. - not to be confused with a Hollywood flop!
Notes: 1999 Film
Lost ~100 million

## Slide 24: Intel Xeon (Server) Architecture Codenames
Number of FLOP/s depends on width, number, and abilities of VPUs in a core
Per-core rates, double precision (64-bit doubles – twice this for 32-bit floats)
  Pentium 4*… Nehalem/Westmere (SSE2… SSE4):
    4 DP FLOPs/cycle: 128-bit addition + 128-bit multiplication
  Sandy Bridge/Ivy Bridge (AVX)
    8 DP FLOPs/cycle: 256-bit addition + 256-bit multiplication
  Haswell/Broadwell (AVX2)
    16 DP FLOPs/cycle: two, 256-bit FMA, fused multiply-add
  KNL/Skylake (AVX-512)
    32 DP FLOPs/cycle: two**, 512-bit FMA
  Cascade Lake (AVX-512 VNNI with INT8)
    32 DP FLOPs/cycle: two, 512-bit FMA
*Pentium III (1999) introduced 128-bit SSE for 4 single-precision floats
**Some Skylake-SPs can do only one 512-bit FMA = (a × b + c), per core
2x
2x
2x
ADD MUL
Notes: Intel Deep Learning Boost (VNNI) provides significant, more efficient deep learning inference acceleration
Combines three AVX-512 instructions (VPMADDUBSW, VPMADDWD, VPADDD) into a single VPDPBUSD operation

## Slide 25: Intel Xeon (Server) Architecture Codenames
Number of FLOP/s depends on width, number, and abilities of VPUs in a core
Per-core rates, double precision (64-bit doubles – twice this for 32-bit floats)
  Nehalem/Westmere (SSE):
    4 DP FLOPs/cycle: 128-bit addition + 128-bit multiplication
  Sandy Bridge/Ivy Bridge (AVX)
    8 DP FLOPs/cycle: 256-bit addition + 256-bit multiplication
  Haswell/Broadwell (AVX2)
    16 DP FLOPs/cycle: two, 256-bit FMA, fused multiply-add
  KNL/Skylake (AVX-512)
    32 DP FLOPs/cycle: two*, 512-bit FMA
  Cascade Lake (AVX-512 VNNI with INT8)
    32 DP FLOPs/cycle: two, 512-bit FMA
2x
2x
2x
*Pentium III (1999) introduced 128-bit SSE for 4 single-precision floats
**Some Skylake-SPs can do only one 512-bit FMA = (a × b + c), per core
Notes: Intel Deep Learning Boost (VNNI) provides significant, more efficient deep learning inference acceleration
Combines three AVX-512 instructions (VPMADDUBSW, VPMADDWD, VPADDD) into a single VPDPBUSD operation

## Slide 26: Outline
Motivation
HPC Cluster
Compute
Memory
  Layout
  Cache
  Performance
Disk
Other Architectures

## Slide 27: Memory Hierarchy
Main Memory (DRAM)
Core
1
L1
L3
L2
Core
2
L1
L2
Core
n
L1
L2
…
UPI
Main Memory (DRAM)
L3
L2
L2
L2
L1
L1
L1
Core
1
Core
2
Core
n
…
Dual Socket Intel Xeon CPU
 | Registers | L1 Cache | L2 Cache | L3 Cache | DRAM | Disk
Speed | 1 cycle | ~4 cycles | ~10 cycles | ~30 cycles | ~200 cycles | 10ms
Size | < KB per core | ~32 KB per core | ~256 KB per core | ~35 MB per socket | ~100 GB per socket | TB
CPU 1
CPU 2
Notes: DDR4 – Double data rate 4th generation (Synchronous dynamic RAM)
UPI – UltraPath Interconnect (Intel) Skylake shifted more L2 cache from shared L3 cache (L2 ~1MB)

## Slide 28: Growth in Memory Performance Lags CPU
http://web.sfc.keio.ac.jp/~rdv/keio/sfc/teaching/architecture/architecture-2008/hennessy-patterson/Ch5-fig02.jpg
Gap grows at 50% per year!
If your data is served by RAM and not caches it doesn’t matter if you have vectorization.
To increase performance, try to minimize memory footprint.
Notes: Memory gap increases…
What do you think should require more attention?

## Slide 29: Outline
Motivation
HPC Cluster
Compute
Memory
Disk
  Types
  Filesystems
Other Architectures

## Slide 30: File I/O
“A supercomputer is a device for turning compute-bound problems into I/O-bound problems.”
-- Ken Batcher, Emeritus Professor of Computer Science at Kent State University

## Slide 31: Types of Disk
Hard Disk Drive (HDD)
  Traditional Spinning Disk
Solid State Drives (SSD)
  ~5x faster than HDD
Non-Volatile Memory Express (NVMe)
  ~5x faster than SSD
Photo Credit: Maximum PC

## Slide 32: Types of Filesystems - NFS
NFS – Network File System
  Simple, cheap, and common
  Single filesystem across network
  Not well suited for large throughput
Storage
Storage
Storage
NFS Server
Head node
Comp node 001
Comp node 002
Comp node N
...
...
≤ 8 storage devices

## Slide 33: Parallel Filesystems
GPFS (General Parallel Filesystem – IBM)
  Designed for parallel read/writes
  Large files spread over multiple storage devices
  Allows concurrent access
  Significantly increase throughput
Lustre
  Similar idea
  Different implementation
Parallel I/O library in software
  Necessary for performance realization
Storage
Storage
Storage
Object Storage
Head node
Comp node 001
Comp node 002
Comp node N
...
...
File A 1/3
File A 2/3
File A 3/3
GPFS Servers
File A
1,000s of storage devices

## Slide 34: Outline
Motivation
HPC Cluster
Compute
Memory
Disk
Other Architectures
  GPUs
  Xeon Phi
  Cloud

## Slide 35: Heterogeneous Systems on the Rise
The computing landscape changes rapidly
60% of TOP500 systems now have accelerators (June 2022)
Graphics processing units (GPUs) are by far the most common type of accelerator
https://www.top500.org/statistics
Notes: NVIDIA P100, Intel Xeon Phi

## Slide 36: GPU and CPU Performance Trends
https://docs.nvidia.com/cuda/archive/9.1/pdf/CUDA_C_Programming_Guide.pdf

## Slide 37: General Purpose GPUs
General Purpose GPU (GPGPU)
  NVIDIA Pascal/Volta/Ampere…
  AMD Radeon Instinct, others
Always attached to a CPU host
  Data travels to device over PCIe
  NVIDIA NVLink has higher speed
Not compatible with x86
Programmable sort-of-like CPUs
  NVIDIA CUDA: extensions to C++
  OpenCL, OpenACC, OpenMP, …
  Need compatible compiler, libraries
NVIDIA Volta V100

## Slide 38: NVIDIA Tesla V100 (V for “Volta”)
80 Streaming Multiprocessors (SMs)
  Analogous to CPU cores
  Execute only SIMD-type instructions
One SM holds many “CUDA cores”
  Analogous to vector lanes
  64 FP32 CUDA cores
  64 INT32 CUDA cores
  32 FP64 CUDA cores
One SM also has 8 tensor cores
  Fast 4x4 matrix multiplications in FP16
Device memory: 32 GB of HBM2
Notes: LD/ST units
FP16 @ 2x SP rate
cc7.0:
TensorCore
4 warp schedulers
Each warp scheduler is dual issue capable
P100: 50 SM’s, 16GB
V100: 80 SM’s, 16/32GB

## Slide 39: NVIDIA Execution Model
SIMT = Single Instruction Multiple Thread
  Operations apply to “warps” of 32 threads
  A warp of threads is like a CPU vector
  Not all that different from SIMD
CUDA core = scalar (thread) processor
  Instructions only go to groups of 32
  A thread block must be split into warps of 32
  Thus, an SM is like 1 or 2 vector units in a CPU
One thread block maps to one SM
A grid of thread blocks can be spread over the entire device
Notes: LD/ST units
FP16 @ 2x SP rate
cc7.0:
TensorCore
4 warp schedulers
Each warp scheduler is dual issue capable
P100: 50 SM’s, 16GB
V100: 80 SM’s, 16/32GB

## Slide 40: R.I.P. Intel Xeon Phi, a.k.a. Intel MIC
MIC: Many Integrated Cores
  x86-compatible multiprocessor architecture
Programmable just CPUs
  MPI, OpenMP, OpenCL, …
  Same compilers as CPUs
But many cores, fast MCDRAM like GPUs
  Intel’s “answer” to the GPU challenge
Started out as a coprocessor
  Data travels over PCIe
  Became main processor in 2nd generation
Eventually merged into Xeon line

## Slide 41: Processors vs. PCIe Devices, Circa 2019
M. Lefebvre
 | Xeon Gold 5122 (2017) | Xeon Platinum 8280M (2019) | Xeon Phi 7290F (2017) | NVIDIA V100 (2017)
Cores | 4 | 28 | 72 | 84 SMs
Logical Cores | 8 | 56 | 288 | 5120 cores
Clock rate | 3.6 – 3.7 GHz | 2.5 – 3.8 GHz | 1.5-1.7 GHz | 1530 MHz
Theoretical GFLOPS (double) | 460.8 | 2240 | 3456 | 7450
SIMD width | 512 bit | 512 bit | 512 bit | Warp of 32 threads
Memory | -- | -- | 16 GB MCDRAM 384 GB DDR4 | 32 GB
Memory B/W | 127.8 GB/s | 127.8 GB/s | 400+ GB/s MCDRAM 115.2 GB/s RAM | 900 GB/s
Approx. Unit Price | $1,200 | $12,000 | $3,400 | $9,000
Notes: https://www.v-t.co.jp/product/wp-content/uploads/sites/2/2017/09/Skylake-SP_Feature_092017.pdf
Choice of xeon is arbitrary (actually depends on the data I could find)

## Slide 42: Demystifying the Cloud
“Regular” computers, just somewhere else
Provide users with remote virtual machines or containers
Can be used for anything:
  Mobile services, website hosting, business applications, …
  Data analysis, high performance computing
Providers
  Amazon Web Services (AWS)
  Microsoft Azure
  Google Cloud Platform (GCP)
  Oracle Cloud
  Lots of others

## Slide 43: Cloud Computing Pros and Cons
Advantages:
  Potentially lower cost
    Pay as you go
    Save on sysadmins and infrastructure
    Economy of scale
  Scaling up or down as needed
    Can be used to run overflow from a regular data center
  Access to a wide range of hardware
Challenges:
  Data movement
    Expensive and time consuming
  Security, privacy, …
Notes: Notice the “potentially”s

## Slide 44: What We Didn’t Talk About
Microarchitecture details (ALU, FPU, pipelining…)
Memory bandwidth and latency
Cache lines and cache coherence
IBM (Power) or AMD processors
FPGAs, Google TPUs, NPUs, …

## Slide 45: Resources & References
Very nice glossary: https://cvw.cac.cornell.edu/main/glossary
J. Hennessy, D. Patterson, Computer Architecture: A Quantitative Approach, 6th edition (2017), ISBN 978-0128119051
U. Drepper, What Every Programmer Should Know About Memory, http://people.redhat.com/drepper/cpumemory.pdf
NVIDIA Volta Architecture Whitepaper https://images.nvidia.com/content/volta-architecture/pdf/volta-architecture-whitepaper.pdf
Notes: Bit.ly/2019-comp-arch